## Slide 1: Kernal 64 A Commodore 64 Scala emulator
2015
Alessandro Abbruzzetti
abbruzze@gmail.com

## Slide 2: What we are not talking about
Scala type system
Scala DSL
Libraries and frameworks
Plug & play components
Category theory
Akka, actors, futures, reactiveness, etc.

## Slide 3: What we’re talking about /1
”In computing, an emulator is hardware or software (or both) that enables one computer system (called the host) to behave like another computer system (called the guest). An emulator typically enables the host system to run software or use peripheral devices designed for the guest system. Emulation refers to the ability of a computer program in an electronic device to emulate (imitate) another program or device.”

## Slide 4: What we’re talking about /2
An emulator:
needs always the original software of the emulated system (often, obtained with a dumping method)
can be useful to:
  combat obsolescence
  have better graphics quality than original hardware
  allow users to play games for discontinued consoles
  add features original hardware didn't have

## Slide 5: Why emulate a Commodore 64 ?
Because it is not easy
Because it is funny
Because there is a huge amount of available software for it
Because, still today, there is an active community of developers and internet sites
Because of the demoscene (http://csdb.dk)

## Slide 6: The Commodore 64 !
Do you remember ?
The "breadbin" model

## Slide 7: Startup screen. Ready (for what ?)

## Slide 8: GEOS OS

## Slide 9: Commodore 64 History /1
The Commodore 64 is an 8-bit home computer introduced in January 1982 by Commodore International. It is listed in the ”Guinness Book of World Records” as the highest-selling single computer model of all time with independent estimates placing the number sold between 10 and 17 million units. More C64s have been sold than any other single computer system, even to this day.
Approximately 10,000 commercial software titles have been made for the Commodore 64 including development tools, office productivity applications, and games
At its peak, GEOS (Graphic Environment Operating System) was the third most popular microcomputer operating system in the world (trailing only MS-DOS and Mac OS)

## Slide 10: Why Scala ?
Because does not exist a C64 emulator written in Scala
Because I love Scala and its ecosystem
Because an emulator written in C/C++ can take advantage of low level operations and ...
Because I was curious about a Scala implementation’s performance

## Slide 11: Kernal64 – A Commodore 64 emulator written in the Scala language
It emulates:
all the main hardware chipset and the memory (RAM/ROM)
all the ”internal” I/O devices, like the keyboard, the monitor, the joysticks, the audio device,...
some external I/O device, like the floppy drive, the magnetic tape data storage device, the printer, the cartridges,...

## Slide 12
Commodore 64 technical information | 
Introduced | January 1982
Released | September 1982
End of production | 1993
How many | ~17 million
Price | US $595
CPU | MOS 6510, ~1MHz
Sound | SID 6581, 3 channels of sound/ 9 octaves, 4 waveforms
RAM | 64K
Display | 25 X 40 text 320 X 200, 16 colors max
Ports | TV, Tape interfarce, User port, 2 joysticks, cartridge port serial peripheral port
Peripherals | cassette recorder, printer, modem,external 170K floppy drive
OS | ROM BASIC V2.0 (Microsoft)

## Slide 13: Where to start from
Internet is the main source of information
A real machine would be welcome
99% of C64 related information is available, but, that 1% cannot be neglected in order to have a reliable and accurate emulator
Every component is hard to emulate, but the VIC (Video Interface Controller) and the Disk Drive are the hardest ones
The circuit diagram is mandatory

## Slide 14: Perhiperals Overview
Expansion Port
UserPort
Control Port
Serial Bus
Cassette Port
PAL/NTSC

## Slide 15: Ok, let’s start digging into details...

## Slide 16: Commodore 64 Circuit Diagram

## Slide 17: Commodore 64 Circuit Diagram
CPU 6510
CIA1 6526
CIA2 6526
VIC
SID
PLA
CHAR ROM
KERNAL & BASIC ROM
RAM
EXPANSION PORT
USER PORT
Control ports
Keyboard
Serial
bus
C2N

## Slide 18: C64 Emulator Block Diagram
6510
C2N
Serial bus
Key board
Control Port #1
Control Port #2
User Port
CIA #1
CIA #2
clk
clk
clk
DRAM
CHAR ROM
BASIC ROM
KERNAL ROM
PLA
SID
VIC II
clk
clk
clk
Clock
clk 985248 Hz
Expansion Port
nmi
irq
rdy
ba
dma
ba
COLOR RAM
exrom
game
Audio Contr.
CRT

## Slide 19: Object Hierarchy
C64Component
C64
Clock
CPU_6510
Expansion Port
IEC
bus
Datassette
CIA
Control Port
CIA1
CIA2
C1541
VIA
VIA IECbus
VIA
DiskCtr
Key
board
MPS 803
SID
VIC
Others
RAMs/ROMs

## Slide 20: Memory

## Slide 21: Memory Layout/1
RAM
RAM
RAM
RAM
$0000
$A000
$C000
$E000
$FFFF
BASIC ROM
CHARROM
$D000
I/O
COLOR RAM
KERNAL ROM
64K RAM
8K BASIC ROM
8K KERNAL ROM
4K CHARACTERS ROM
1000 nibbles COLOR RAM
the operating system

## Slide 22: Memory Layout/2
CHARACTERS ROM
VIC-II
$D000
SID
COLOR RAM
CIA1
CIA2
I/O1
I/O2
$D400
$D800
$DC00/ $DD00
$DE00/ $DF00
Video Controller
Audio Controller
Color RAM
Complex Interface Adapters
I/O Open Address Space

## Slide 23: The Memory trait
trait Memory {
val isRom: Boolean
val length: Int
val startAddress: Int
lazy val endAddress = startAddress + length
val name: String
def init
def isActive: Boolean
def read(address: Int, chipID: ChipID.ID = ChipID.CPU): Int
def write(address: Int, value: Int, chipID: ChipID.ID = ChipID.CPU)
}

## Slide 24: The BridgeMemory class
abstract class BridgeMemory extends Memory {
private[this] var bridges : List[(Int,Int,Memory)] = Nil
...
def addBridge(m:Memory) { … }
@inline private def select(address:Int) : Memory = { … }
final def read(address: Int, chipID: ChipID.ID = ChipID.CPU): Int = select(address).read(address,chipID)
final def write(address: Int, value: Int, chipID: ChipID.ID = ChipID.CPU) =
select(address).write(address,value,chipID)
}

## Slide 25: Memory implementation /1
6510 Memory
BASIC ROM
VIC
CIA1
CIA2
RAM
Read $A000
Write$D000
Read $DC00
CHAR ROM
Not active
Not active
I/O Bridge
Composite pattern
PLA

## Slide 26: Memory implementation /2
Advantages
  Modularity
  Isolation
  Ease of modification
Disadvantages
  Performance bottleneck

## Slide 27: Clock

## Slide 28: Clock frequency
φ1
φ2
Clock frequency is 985248 Hz
During φ1 phase the VIC chip accesses the bus
During φ2 phase the 6510 chip accesses the bus
To emulate the real speed of the C64 the emulator will be able to process about a million cycles per second

## Slide 29: Clock – one thread model
The emulator has a single source of synchronization, the clock, like real HW
The clock is managed by one thread
If the thread is preempted by the host cpu, the emulator slows down
Multithread model is very difficult to realize (the C64 6510 cpu running on T1 and the 1541 disk drive 6502 cpu runing on T2)

## Slide 30: Emulator main loop /1
cycles/sec
Δ
delay
985248 reference cycles
Core sequence
Clock’s Thread Loop
calibration

## Slide 31: Emulator main loop /2
Scheduler
VIC φ1
Bus devices
  Disk drives
  Printer
CPU φ2
A clock cycle is consumed by every component that needs it

## Slide 32: Scheduler
It manages a linked list of ordered future events. The time, in the emulator’s world, is discrete and its value is determined by the number of elapsed cycles.
when
what to do
next
cycles time
0
x
Function2[Long] → Unit

## Slide 33: Clock ins and outs
class Clock private (errorHandler:Option[(Throwable) =>Unit], name:String = "Clock")(mainLoop: (Long) => Unit) extends Thread(name) with C64Component {
private class ClockEvent (val id : String, val when : Long, val execute: (Long) => Unit)
private class EventList(val e:ClockEvent, var next:EventList = null)
private[this] var events : EventList = null private[this] var cycles = 0L
}

## Slide 34: CPU

## Slide 35: 6510 opcodes & cycles

## Slide 36: 6510 opcode execution flow
Fetch
MEMORY
RDY?
Decode
Execute
INT?
op1
...
opN
Interrupt Handler
RDY?
no
no
PC
A
X
Y
SP
FLAGS
micro program

## Slide 37: Main components

## Slide 38: Main component – CPU 6510
PC
A
X
Y
SP
FLAGS
LDA1
Current state
LDAn
...
STA1
...
STAk
...
RTS1
...
RTSm
Function1[Unit]
micro states
Ready signal
MEMORY
R/W
IRQs

## Slide 39: Main component – CIA 6526
Scheduler
events
Timer A
Timer B
State machine - control Logic
Data Port
External devices
MEMORY
I/O
mapped
TOD

## Slide 40: Main component – SID 6581
javax.sound.
sampled.AudioDriver
44kHz sampling,
mono
MEMORY
I/O
mapped
ReSID library
Scheduler

## Slide 41: Main component – VIC 6567(9)
RASTER MANAGEMENT PAL = 312 lines
Video Matrix Management
Sprites Management
Graphics Data Sequencer
Sprites Data Sequencer
MUX Sprite priorities and collision detection
Border Unit
IRQ MANAGEMENT (lightpen,collisions, raster)
JPanel +
java.awt.image. MemoryImageSource
16K Bank
I/O
mapped
COLOR RAM

## Slide 42: Display

## Slide 43: 1541 Block Diagram
Motor & R/W logic
IEC BUS
ATN
CLK
DAT
PLA
2K RAM
DOS ROM
IRQ
SO
300 RPM
GCR (Group code recording)
D64
dump

## Slide 44: 1541 – floppy disk layout
300 RPM

## Slide 45: 1541 – disk zones

## Slide 46: Exchanging data with drive C1541
C1541
Drive
C64
CIA2
Port B
Port A
IEC Bus
CPU
6510
CPU
6502
User Port
clock
data
0 0 1 0
VIA IEC Bus

## Slide 47: CIA2 data port A spec.
Address range: $DD00-$DDFF, 56576-56831 Tasks: Serial bus, RS-232, VIC memory, NMI control |  |  |  | 
Address Hex | Address Dec | Register | Function | Remark
$DD00 | 56576 | 0 PRA | Data Port A | Bit 0..1: Select the position of the VIC-memory %00, 0: Bank 3: $C000-$FFFF, 49152-65535 %01, 1: Bank 2: $8000-$BFFF, 32768-49151 %10, 2: Bank 1: $4000-$7FFF, 16384-32767 %11, 3: Bank 0: $0000-$3FFF, 0-16383 (standard) Bit 2: RS-232: TXD Output, userport: Data PA 2 (pin M) Bit 3..5: serial bus Output (0=High/Inactive, 1=Low/Active) Bit 3: ATN OUT Bit 4: CLOCK OUT Bit 5: DATA OUT Bit 6..7: serial bus Input (0=Low/Active, 1=High/Inactive) Bit 6: CLOCK IN Bit 7: DATA IN
... | ... | ... | ... | …

## Slide 48: CIA2 port A implementation
class PortAConnector(mem:BankedMemory,bus:IECBus,rs232:RS232) extends Connector with IECBusListener {
…
val busid = "CIA2_PortA"
import IECBus.bus._
final def read : Int =
(~((clk << 6) | (data << 7)) & 0xC0) | (latch & 0x3C) | bank | rs232.getTXD << 2
final protected def performWrite(data:Int) = {
val value = data | ~ddr
bank = value & 3
mem.setBank(bank)
bus.setLine(busid,if ((value & 8) > 0) GROUND else VOLTAGE, // ATN
if ((value & 32) > 0) GROUND else VOLTAGE, // DATA
if ((value & 16) > 0) GROUND else VOLTAGE) // CLOCK
if ((ddr & 4) > 0) rs232.setTXD((data >> 2) & 1)
}
}
RAM
$0000
$DD00
$FFFF

## Slide 49: Let’s connect to BBS via Internet! http://cbbsoutpost.servebbs.com/
Bulletin Board System are still alive.
BBS now use the telnet protocol instead of modems
SwiftLink cartridge implementation

## Slide 50: Scala performance notes
Avoid private val/var x when possible, use private[this] val/var x instead
Use @inline annotation
Avoid for loops. Use while loops instead
Avoid by name parameters

## Slide 51: DEMO
Turrican II (1991 by Rainbow Arts)
Comaland (Censor Design, Oxyron), a demo from X’2014 Demo Competition (it won the compo!)

## Slide 52: def Q&A(q:Query) : Option[Answer]

## Slide 53: THANK YOU!
2015